## Slide 1: Raspberry Pi GPIO + MCS Cloud

## Slide 2: DHT-11 溫溼度感應器

## Slide 3: Reference
http://yehnan.blogspot.tw/2015/05/raspberry-pidht11.html

## Slide 4: Packages
先安裝所需套件： $ sudo apt-get update $ sudo apt-get install build-essential python-dev 然後下載，進入該目錄： $ git clone https://github.com/adafruit/Adafruit_Python_DHT.git $ cd Adafruit_Python_DHT 安裝： $ sudo python setup.py install 接著就能讀取DHT11了，執行寫好的範例Python程式： $ cd examples $ sudo ./AdafruitDHT.py 11 4 Temp=27.0*C Humidity=81.0% 其中參數11代表DHT11，4代表我把它接到Raspberry Pi的GPIO 4。

## Slide 5: Modify AdafruitDHT.py
# Try to grab a sensor reading. Use the read_retry method which will retry up
# to 15 times to get a sensor reading (waiting 2 seconds between each retry).
humidity, temperature = Adafruit_DHT.read_retry(sensor, pin)
# Un-comment the line below to convert the temperature to Fahrenheit.
# temperature = temperature * 9/5.0 + 32
# Note that sometimes you won't get a reading and
# the results will be null (because Linux can't
# guarantee the timing of calls to read the sensor).
# If this happens try again!
if humidity is not None and temperature is not None:
print('Temp={0:0.1f}* Humidity={1:0.1f}%'.format(temperature, humidity))
else:
print('Failed to get reading. Try again!')
sys.exit(1)

## Slide 6: Modify AdafruitDHT.py
While true:
  humidity, temperature = Adafruit_DHT.read_retry(sensor, pin)
  if humidity is not None and temperature is not None:
    print('Temp={0:0.1f}* Humidity={1:0.1f}%'.format(temperature, humidity))
  else:
    print('Failed to get reading. Try again!')
    sys.exit(1)

## Slide 7: CHECK POINT #1
讓 DHT-11 可以一直量測溫溼度

## Slide 8: MCS Cloud

## Slide 9: Reference
http://oranwind.org/-linkit-smart-7688-chuan-song-sensor-data-dao-mediatek-cloud-sandbox-mcs/

## Slide 10: MediaTek Cloud Sandbox (MCS) 端

## Slide 11: Step 1:
到 MediaTek Cloud Sandbox (MCS) 網站申請帳號
https://mcs.mediatek.com

## Slide 12: Step 2: Login

## Slide 13: Step 3:點擊 開始

## Slide 14: Step 4: 開發 -> 產品原型

## Slide 15: Step 5.
輸入 產品原型名稱、產品原型版本、硬體平台、產業、應用程式 再按儲存
硬體平台raspberry pi

## Slide 17: Step 6
點擊 Last updated prototype 中的 raspberry pi

## Slide 18: Step 7 Add Data Channel

## Slide 19: Step 8. Display -> Add

## Slide 20: Step 9
輸入 Temperature 的 Data channel name、Data channel Id、Data type、Unit 再按 Save

## Slide 22: Step 10
Repeat Step 7 – 8.
Add data channel

## Slide 23: Step 11
輸入 Humidity 的 Data channel name、Data channel Id、Data type、Unit 再按 Save

## Slide 25: Step 12
點擊 Create Test device 輸入 raspberry pi

## Slide 26
點擊下方 裝置 中的 Raspberry Pi
取得 DeviceId 與 DeviceKey

## Slide 28: Step 13 – Modify AdafruitDHT.py add post_to_mcs function
import time
import sys
import httplib, urllib
import json
deviceId = "D2WKWKcr “
deviceKey = “LcWuC5DykgbM5fqS“
def post_to_mcs(payload):
headers = {"Content-type": "application/json", "deviceKey": deviceKey}
not_connected = 1
while (not_connected):
try:
conn = httplib.HTTPConnection("api.mediatek.com:80")
conn.connect()
not_connected = 0
except (httplib.HTTPException, socket.error) as ex:
print "Error: %s" % ex time.sleep(10)
# sleep 10 seconds
conn.request("POST", "/mcs/v2/devices/" + deviceId + "/datapoints", json.dumps(payload), headers)
response = conn.getresponse()
print( response.status, response.reason, json.dumps(payload), time.strftime("%c"))
data = response.read()
conn.close()

## Slide 29: Modify AdafruitDHT.py
While true:
  h0, t0= Adafruit_DHT.read_retry(sensor, pin)
  if humidity is not None and temperature is not None:
    print('Temp={0:0.1f}* Humidity={1:0.1f}%'.format(temperature, humidity))
payload = {"datapoints":[{"dataChnId":"Humidity","values":{"value":h0}},
{"dataChnId":"Temperature","values":{"value":t0}}]}
post_to_mcs(payload)
time.sleep(10)
  else:
    print('Failed to get reading. Try again!')
    sys.exit(1)

## Slide 31: CHECK POINT 2
MCS Cloud 持續顯示溫濕度

## Slide 32: MCS Cloud 顯示開關狀態

## Slide 33: 新增資料通道 -> 顯示器

## Slide 34: 資料型態 -> 開關

## Slide 35: Python 讀取 GPIO 狀態

## Slide 36: 將開關狀態上傳 MCS Cloud

## Slide 37: CHECK POINT 3
MCS Cloud 持續顯示溫濕度及開關狀態

## Slide 38: MCS Cloud 控制 LED

## Slide 39: 新增資料通道 控制器

## Slide 40: 資料通道 -> LEDControl

## Slide 41: Reference
http://draw-bruce.blogspot.tw/2016/01/iot10-mediatek-cloud-sandbox.html

## Slide 42: CHECK POINT 4
MCS Cloud 直接控制 LED